SPECIFICATION

产品规格书

客户名称Customer:

产品名称Product Name:         开关电源 slim switching power supply

型号规格Part Number:        YY-D-360-12   E系

文件编号 File NO:

日    期 Date:                          数量Quantity：

| PREPARED BY 编写 | CHECKEN BY 审核 | APPROVED BY 批准 | CustomerApproval 客户确认 |
| --- | --- | --- | --- |

承认签章后请寄回承认书正本一份

Please return to us one original of “SPECIFICATION FOR APPROVAL” with your approved signatures

安徽省友谊电子有限公司

ANHUI YOUYI ELECTRONICS CO.，LTD

地址：安徽省天长市秦栏工园区一号

Add: No.1,Industrial Zone,Qinlan,Tianchang City,Anhui Province,China

Tel:0550-7811225       Fax：0550-7812288

http://www.you-yi.com

Revision History

修订履历

| Revision 版本 | Change ltem 修改项次 | APPROVED BY 批准 | Date 修改日期 |
| --- | --- | --- | --- |
| 备注：针对本系列产品输出12V/30A规格说明. |

Content

目录

1 修订履历 Revision History :	2

2 产品概述Product Overview:	4

2 电气规格 Electrical Specification:	4

2.1 输入特性 Input Electrical Characteristics:	4

2.2工作电压降额曲线Operate voltage rating Cuidline:	4

3 输出特性 Output Electrical Characteristics:	5

3.1工作温度曲线Operate temperature rating Cuidline:	5

3.2输出电压曲线Output viltage curve:	5

3.3 输出电压电流 Output voltage & Current Regulation:	6

3.4开机延迟时间 Power on delay time:	6

3.5 输出动态响应Output Transient Response:	6

3.6输出上升时间 DC output voltage rise time:	6

3.7输出纹波和噪声 DC Output Ripple & Noise:	7

4 保护功能 Protection:	7

4.1输出短路保护DC Output Short Circuit Protection:	7

4.2输出过流保护DC Output Over Load Protection:	7

4.3过温保护Over temperature Protection:	7

5绝缘性能Isolation:	8

5.1绝缘耐压Dielectric Strength:	8

5.2绝缘阻抗 Insulation Resistance:	8

6电磁兼容性 EMC:	8

6.1电磁干扰EMI:	8

6.2电磁抗扰 EMS:	8

7工作环境 Environmental Requirement:	9

7.1环境温度Temperature:	9

7.2环境湿度Humidity:	9

7.2海拔高度Altitud:	9

8冲击&振动耐受Vibration:	9

9冷却方式Cooling Method:	9

10平均故障间隔时间 MTBF:	9

11产品重量Weight:	9

12链接端子定义Pin Connection:	10

13电源安装尺寸Power Supply Mounting dimension:	11

14使用注意事项:	11

15包装、运输、贮存:	11

15.1包装:	11

15.2运输:	11

14.3贮存:	11

## 1：产品品概述Product Overview

本产品为 AC-DC恒压电源供应器，适用于多数工业直流供电设备，如显示屏等…,具有效率高、体积小、稳定以及高可靠性等特点；电源具有各种完善的保护功能，如输出短路、过温保护…

## 2：电气规格 Electrical Specification。

## 2.1输入特性 Input Electrical Characteristics。

| 型号model 项目Project | YY-D-360-12 E系 |
| --- | --- |
| 额定功率 Normal output power | 360W |
| 正常输入电压 Normal voltage range | 200 Vac ~240Vac |
| 输入电压范围 Intput voltage range | 176 Vac ~264Vac |
| 频率范围 Frequency range最大 | 47HZ~63HZ |
| 功率因数 PF | ≥0.5 |
| 漏电流 Leakage Current | ≤0.25ma,@220Vac |
| 最大输入电流 Max intput ac current | 3A |
| 浪涌电流 Inrush current | ≤60A,@220Vac |
| 效率(满载) Efficiency(full load) | ≥85% |

## 2.2工作电压降额曲线Operate voltage rating Cuidline.

输入电压(Vac)

## 3：输出特性 Output Electrical Characteristics

## 3.1工作温度曲线Operate temperature rating Cuidline.

产品工作环境温度(℃)

Operating environment temperature

如产品工作处在-25℃以下环境，让电源启动带负责≤10%工作5～10分钟后便可正常使用。

## 3.2输出电压曲线Output viltage curve

输出电压Vdc

## 3.3输出电压电流 Output voltage & Current Regulation

| 型号model 项目Project | YY-D-360-12 E系 |
| --- | --- |
| 输出电压 Output Voltage | 12Vdc |
| 设定精度（空载） Setting | ±0.1V |
| 输出额定电流 Output Rated Current | 30A |
| 峰值电流 Peak Current | 33A |
| 调整率 Regulation | ±3% |

## 3.4开机延迟时间 Power on delay time

| 延迟时间delay time 输出电压Output Voltage | 220Vac Intput @ -40～-5℃ | 220Vac Intput @ ≥25℃ |
| --- | --- | --- |
| 12Vdc | ≤5S | ≤3S |
| -- | - | - |

## 3.5输出动态响应Output Transient Response

| 变化速率 Slew Rate | 电压变化范围 Voltage Limit | 负载变化 Load Change |
| --- | --- | --- |
| 12Vdc | 1～1.5A/uS | ≤±5% | 从最小值到50%和从50%到最大值 @Min.to 50% load and 50% to max load |
| - | - | - |  |

## 3.6输出上升时间 DC output voltage rise time

| 输出电压 Output Voltage | 输入220Vac 带满载启 220Vac input & full load | 标注说明 Note |
| --- | --- | --- |
| 12Vdc | ≤50mS | 上升时间为输出电压从10%上升到90%段的时间 The rise time measured is when the output voltages rise from 10% to 90% of specified output voltage Vout observed on the channel waveform. |
| - | - |  |

## 3.7输出纹波和噪声 DC Output Ripple & Noise

| 输出电压 Output Voltage | 纹波和噪声 Ripple & Nnoise |
| --- | --- |
| 12Vdc | 270mVp-p@25℃ |
|  | 360mVp-p@-25℃ |
| - | - |
|  | - |
| - | - |
|  | - |

测试说明 Note

A.纹波和噪声测试：纹波和噪声测试带宽设置在20mHZ.

Ripple & Nnoise test：Ripple & Nnoise bandwidth is set to 20mHZ.

B.测试纹波和噪声时要在输出端并联1个0.1UF瓷片电容和一个10UF电解电容

Use a 0.1uf ceramic capacitor in parallel with a 10uf eaectrolyic capacitor at output connector terminals for ripple & noise measurements.

## 4：保护功能 Protection

## 4.1输出短路保护DC Output Short Circuit Protection

| 输出电压 Output Voltage | Comments |
| --- | --- |
| 12Vdc | 短路时关闭输出，故障排除自恢复工作 Output will be stopped when the circuit is shorted and restart operating after eliminating malfunction |

## 4.2输出过流保护DC Output Over Load Protection

| 输出电压 Output Voltage | Comments |
| --- | --- |
| 12Vdc | 输出电流超过额定值105～30%，并闭输出，故障排除后自恢复工作 Output will be stopped when the DC current is more than 105～30% of rated current and restart operating after eliminating malfunction |

## 4.3过温保护Over temperature Protection

| 输出电压 Output Voltage | Comments |
| --- | --- |
| 12Vdc | 产品温度达到设定值，并闭输出，故障排除后自恢复工作 Output will be stopped when the temperature reaches the set value and restart operating after eliminating malfunction |

## 5：绝缘性能Isolation

## 5.1绝缘耐压Dielectric Strength

| 输入对输出(Input To Output) | 50Hz 2750Vac交流档测试1分钟，漏电流≤5mA 。 2750Vac 50HZ 1minute ≤5mA |
| --- | --- |
| 输入对壳(Input To FG) | 50Hz 1500Vac交流档测试1分钟，漏电流≤5mA 。 1500Vac 50HZ 1minute ≤5mA |

## 5.2绝缘阻抗 Insulation Resistance

| 输入对输出Input To Output | 直流500V测试绝缘阻值最小值不能小于10MΩ DC 500V 10MΩ Min (at room temperature) |
| --- | --- |
| 输出对壳Output To FG | 直流500V测试绝缘阻值最小值不能小于10MΩ DC 500V 10MΩ Min (at room temperature) |
| 输入对壳Input To FG | 直流500V测试绝缘阻值最小值不能小于10MΩ DC 500V 10MΩ Min (at room temperature) |

## 6：电磁兼容性 EMC

## 6.1电磁干扰EMI

电源电磁干扰符合以下标准 The power supply shall comply whth the following criterion.

- 传导干扰度 Conduciton Emission

EN55022,CLASS A

- 辐射干扰度

EN55022,CLASS A

说明：若是客户有需要，可以配合在客户的整机上进行更改,达到标准。

Note：Youyi power can word together with customer to modify the power and the system to meet above crierion

## 6.2电磁抗扰 EMS

A．静电抗扰度ESD

*GB17626.2-1998/IEC61000-4-2    Lever 3     A

A．浪涌SURGE

*GB16726.5-1998/IEC61000-4-5    Lever 3     B

C．电压跌落 DIP

*GB17626.11-1998/IEC61000-4-11

## 7：工作环境 Environmental Requirement

## 7.1环境温度Temperature

A．工作温度Operating:-25℃～+60℃

说明:产品在-25度低温均能够开机工作

Note:The power can power on and work @ -25℃

B．存储温度Storage:-40℃to+70℃

## 7.2环境湿度Humidity

A．工作湿度Operating:从15RH到90RH.

From 15RH to 90RH relative humidity(non-condensing).

B．存储湿度Operating:从10RH到95RH.

From 5RH to 95RH relative humidity(non-condensing).

## 7.3海拔高度Altitude

Operating:0 to 3000m

## 8：耐冲击&振动Shock & Vibration

- 耐冲击：49m/s2(5G),11ms,once each X,Y and Z axis.

- 耐振动10-55Hz,19.6m/s2(2G),20minutes each along X,Y and Z axis.

## 9：冷却方式Cooling Method:

自然冷却Natural cooling

产品依靠其铝合金外壳自然冷却，因此用户安装时应注意避免产品周围5cm内不能有遮挡物，以免影响产品散热。

Custom should avoid to place obstacle inside the 5cm of product surrounding in order to push cooling itself, because the product is cooled by natural air through the Aluminum Alloy Cabinet.

特别注意事项 Specific cautions

- 产品在安装时，安装面可悬空或安装于金属面上，应避免安装面被塑料或木质等非导热材料接触遮挡。

A.    The product should be suspended in air or placed on the face of metal when assembled, and be avoided to place on the face of non-conducting heat materials such as, plastics, board and so on.

- 产品在安装时，模块间距离应控制在大于5cm，避免相互间影响散热。

B.    The space between each module should be exceeded 5cm in order to avoid affecting cooling of each other

## 10：平均故障间隔时间 MTBF

在满负荷25℃环境温度的工作情况下，平均故障间隔时间至少5万小时.

The MTBF shall be at least 50,000 hours at 25℃,full load and normal input condition.

## 11：产品重量Weight

重量Weight： 430g

## 12：链接端子定义Pin Connection

下图是产品俯视图.

外形尺寸：长×宽×高=200×98×42mm

Outside dimension : L*W*H=200×98×42mm

表1为交流输入接线端（PIN距9.5mm）

Table 1 : Input terminal block (pitch 9.5mm)

| 名称 Name | 功能 Function |
| --- | --- |
| L | 交流输入L线 The AC Input Line L |
| N | 交流输入N线 The AC Input Line N |
|  | 接地线 Earth Line |

表2为直流输出接线端 (PIN距9.5mm)

Table 2 ：Output terminal block （pitch 9.5mm）

说明：输出每对端子，其通过最大电流为25A,切勿超载测试和使用，否则会因过流发热，损坏该端子！

Current through the output terminal block should not exceed 25A, so never overload test and work in that kind of condition. Or the terminal block will be damaged because of high temperature.

| 名称 Name | 功能 Function |
| --- | --- |
| V+ V+ V+ | 直流输出正极 Output DC positive pole |
| V- V- V- | 直流输出负极Output DC negative pole |

## 13：电源安装尺寸Power Supply Mounting dimension

下图为产品安装孔位图

The figure below is mounting hole position

Unit:mm

提示：上图为底壳安装孔位图：

方式1.底壳上有4个攻丝孔应用M3机牙螺丝。

Method 1. M3 Machine Screws are suitable for 4 tapped holes under the cabinet.

方式2.底壳上4个U槽应用M3螺丝锁在安装架上。

Method 2. M3 screws lock in the mounting rack of 4 U grooves under the cabinet.

安装时，以上两种安装方式选其一，固定螺丝进入电源本体的长度不能超过 3mm，在拧螺丝时，不可太用力，以免滑丝。

One way should be chosen from the two methods, make sure that the part of screw that is in the body of power supply should be less than 3mm and exert not much strength to avoid damaging the screw.

## 14：使用注意事项 Precautions for use

电源使用须注安全绝缘，各连接线头需要绝缘处理；产品要良好接地，避免用手接触机壳，以免烫伤。

The power supply must work at the condition of insulation and terminal post of cable have to go through the insulation treatment. Besides, make sure the product is grounded well and forbid touching the cabinet in order to avoid scalding hand.

## 15：包装、运输、贮存 Packaging, Transport, Storage

## 15.1包装：包装箱上有产品名称、型号、厂家标识、厂家质量部门的检验合格证、制造日期等；包装箱内有附件清单。

Packaging: The Product name, Model, Manufacturer mark, Inspection certificate from manufacturers quality department and production data should be recorded in the manifest which is inside the package.

## 15.2运输 ：适应于车、船、飞机运输，运输中应遮蓬、防晒、防水、文明装卸。

## Transport: the car transport, shipment, aircraft transport is suitable and make sure that the products are under the condition of sunscreen and waterproof. The products should handle with care when loading or unloading.

## 15.3贮存 ：产品未使用时应存放在包装箱内，仓库环境温度为 -10℃—+80℃，相对湿度为≤80%RH，避免存放在具有腐蚀性气体，并且无强烈的机械振动，冲击和强磁场的环境下，包装箱应垫离地至少 25cm 高，在本规定条件下的贮存期一般为 2 年，超过 2 年后应重新进检验。

Storage: It will be better that the product store in the environment temperature between        -10℃ and +80℃ as well as the humidity less than 80%RH. Make sure that there is no corrosive gases in the store environment. Besides, the surrounding must not have the strong mechanical vibration and high-intensity magnetic field. And the case have to be block up at least 25cm away from the earth. The regulation mentioned above will let the products store for 2 years, power supply should be tested after 2 years.

# Text boxes

负载(%)

负载(%)

输出电流

A